4 CORNER FLOATAIR BOATLIFT OPERATION

(lifts 10000#s + have two motor units)

- BRING BOAT OVER LIFT.

- HOOK YELLOW ROPES (on dock) ONTO BOAT CLEATS.

- TURN YELLOW HANDLED VALVE(S) TO RAISE POSITION,

- TURN SWITCH(ES) ON.

- GET ON DOCK AT FRONT OF BOAT AND PUSH BOAT STRAIGHT BACK UNTIL ROPES ARE TAUT.

- HOLD BOAT UNTIL YOU FEEL LIFT CATCH BOAT, BRINGING BOAT UP AND FORWARD.  LET GO OF BOAT, LIFT WILL DO THE REST.

- WHEN LIFT HAS BOAT RAISED OUT OF WATER, TURN YELLOW HANDLE(S) TO STORE POSITION AND TURN SWITCH(ES) OFF.   (WHEN BUBBLES BLOW OUT FROM UNDER LIFT, LIFT IS AT MAXIMUM HEIGHT.)

LOWERING FLOATAIR….

- TURN YELLOW HANDLE(S) TO LOWER POSITION

DO NOT TURN ON SWITCH(ES)  WHEN LOWERING LIFT

- WHEN AIR STOPS COMING OUT OF BLOWER(S) AND YELLOW ROPES ARE SLACK, TAKE YELLOW ROPES OFF THE CLEATS AND PLACE ON DOCK.

- ENJOY BOATING!!

# Text boxes

Seven Seas Corporation

127 Henry Street

Greenville, SC 29609

(864) 467-1806

(864)467-1896 (fax)

info@boatlifts-floatair.com

www.boatlifts-floatair.com